## Slide 1
Prototype development of cryogenic bolometer for Neutrinoless Double beta decay
TIFR, BARC, VECC, IIT (Ropar), Univ. of Lucknow
The India-based TIN detector (Tin.Tin)
http://www.tifr.res.in/~tin.tin/

## Slide 2
Nuclear Double Beta Decay
ZA
Z1A
Z2A
2n : 2nd order weak interaction, normal beta decay (n) suppressed by Q-value or J
Neutrinoless Double Beta Decay
0n : Lepton number violating process occurs if neutrinos have mass and are their own antiparticles
test the true nature of neutrino Dirac/Majorana
the measurement of effective neutrino Majorana mass.
02 [phase-space ( Q5)]  [Nuclear ME] 2  | m |2

## Slide 3
02 [phase-space ( Q5)]  [Nuclear ME] 2  | m |2
Simultaneous emission of two electrons
Constancy of the sum energy of the two emitted electrons
Sum energy peak  High resolution
Extremely low event rates  very large sources and detector
}
Identification experiments
High Q2 and abundance desirable
Active source (DBD nuclei integral part of the detector)
Passive Source (DBD source external to the detector)

## Slide 4
Underground location (reduce cosmic ray background)
Careful choice of materials (detector & environs- 235,238U, 232Th,40K, radiative impurities) and shielding
Electronic rejection of background events
Neutron background minimization (U/Th induced and muon induced)
For a conclusive proof, 0nbb measurement in several isotopes is essential
Nbkg= B(c/kev/t) • DE • t
Nonbb~√ Nbkg
Background reduction
Experimental Considerations
2nbb detected in several (~12) nuclei, half life measured.
Improvement in sensitivity possible by background reduction in some cases
No 0nbb observed
Present Status
Small scale experiments ~ kg ; T ½ ~1024- 1025 years, <mn> ~0.75 eV
Many new experiments (~ton scale) are planned/proposed, R&D in progress

## Slide 5
Experiment | Isotope | Qbb (MeV) | Technique | Expected <mee>(meV)*
GERDA | 76Ge | 2039.6 | Semiconductor HPGe detector; good energy resolution and efficiency | 15-35
MAJORANA | 76Ge | 2039.6 | Semiconductor HPGe detector; good energy resolution and efficiency | 15-35
SuperNEMO | 82Se | 2995.0 | Tracking + calorimeter; Good background rejection Possibility of DBD in multiple isotopes (150Nd) | 44-140
LUCIFER | 82Se | 2995.0 | Scintillating bolometer; Good energy resolution and efficiency | ~76
AMoRE | 100Mo | 3034.0 | Scintillating bolometer, Good energy resolution and efficiency | 20-60
MOON | 100Mo | 3034.0 | Tracking + Scintillator; Background rejection | ~100
COBRA | 116Cd | 2802.0 | CdZnTe Semiconductor detector; good energy resolution, particle ID | 
CUORE | 130Te | 2533.0 | Cryogenic bolometer, Good energy resolution and efficiency | 50-130
EXO | 136Xe | 2479.0 | liquid TPC, ionization + scintillation; high efficiency, Particle ID, daughter identification (136Ba) proposed | 14-33
KamLAND-Zen | 136Xe | 2479.0 | liquid Scintillator, ultra-low background | 25-60
Major ongoing and proposed 0nbb experiments.
*for about 5-10 years of running time for full scale detector.
Current Science 112, 1375 (2017)

## Slide 6
Best sensitivity limits at (90% C.L.) for current 0nbb experiments:
KamLANDZen (136Xe):
GERDA (76Ge):
CUORE (130Te):
Sergei Petcov, doi: 10.5281/zenodo.4134015
Effective Majorana mass as a function of lightest neutrino mass

## Slide 7
Initiative for DBD experiment in India
Proposal for an experiment at site of the INO
124Sn: T1/2 > (0.8-1.2) x 1021 yrs Nucl. Phys. A 807, 269(2008)
A multi-institutional effort
124Sn (Q =2292.64  0.39 keV)
Sn has TC ~ 3.7 K
Electronic specific heat falls off exponentially below TC
Only lattice specific heat (~T3) present below ~ 500 mK
Z=50 shell is closed
Simple metallurgy
Strongly Multi-disciplinary project
Nuclear Physics, Particle Physics, Low Temperature Physics, Material Science, Physical Chemistry

## Slide 8
A bolometer is a calorimetric detector.
Energy of particle  Thermal energy in detector  measurable temperature rise if net heat capacity is very low
Bolometer Schematic
T0
CD
CS
R1
R2
Incident Energy
TS
t
Sensor- contact
Pulse decay time
Low Temperature Bolometry
Challenge: to make measurements in time domain at mK temperature
Resolution of Bolometer
Limited by Thermodynamical fluctuation noise {dE=(kT2C(T))1/2}
Depends only on operating temperature and specific heat
Independent of incident Energy

## Slide 9
Make a natural Sn bolometric detector ~ 0.51 Kg (TIFR, BARC)
Radiation background studies (TIFR, IIT -Ropar)
Detector and background simulations (TIFR, IIT- Ropar)
Sensor development (TIFR, BARC)
Reliable NTME calculations (Univ. of Lucknow, IIT-KGP, PRL)
Precision Q value measurement (VECC), (Qbb = 2292.64  0.39 keV)
Enrichment of 124Sn (collaboration with Russia?)
Constraining NTME, GT measurement in NDBD nuclei
Work plan
Strongly Multi-disciplinary project
Nuclear Physics, Neutrino Physics, Low Temperature Physics, Material Science, Physical Chemistry

## Slide 10
Cryogen free dilution refrigerator installed at TIFR
Base Temp. ~7 mK
cooling power
1.4 mW@120mK
V. Singh et. al. Pramana 81 (2013) 719

## Slide 11: Thermometer
Energy deposited by Particle  Heat
 rise in Temperature -  T  read by thermometer
phonons
thermometer
°
Change in physical property – e.g. resistance with T
thermal neutrons
Ge
71Ge, 75Ge  decay As, Se, Ga
R (T) = R0 exp( T0/T)0.5

## Slide 12
NTD Ge Sensor R&D
  Neutron irradiation at Dhurva Reactor (BARC, Mumbai)
Isotope | Isotopic Abundance (%) |  | Products (half-life) | Stable end product ( mode) | Dopant Type
 | Set 1 | Set 2 |  |  | 
70Ge | 21.5 | 21.9 | 71Ge* (11.43d) | 71Ga (e- capture) | p
72Ge | 26.8 | 27.0 | 73Ge (stable ) | 73Ge | -
73Ge | 10.8 | 8.8 | 74Ge (stable ) | 74Ge | -
74Ge | 34.1 | 35.1 | 75Ge* (82.78min) | 75As (β-decay) | n
76Ge | 6.8 | 7.2 | 77Ge* (11.3,38.8hrs) | 77As*,77Se (β-decay) | n
Radioactive impurity studies (~2 year cooldown period)
Fast neutron induced defect studies (PALS, Channeling)
  Annealing at 600 oC for 2 hrs in vacuum cures defects
Sensor Fabrication
S. Mathimalar et. al., NIM A 774 (2015) 68,
S. Mathimalar et. al. NIM B 345 (2015) 33.

## Slide 13
Mechanical polishing setup
NTD Ge fabrication & characterisation
Wire bonding machine
Mask for NTD Ge

## Slide 14
Resistance of the NTD Ge samples were measured in the temperature range 100 mK – 350 mK
Characterization of NTD Ge at T < 300 mK
For NTD Ge
(E. Pasca et al., Proc. 8th Int. Conf. Adv. Tech. Part. Phys. 2 (2004) 93)
depends on intrinsic properties of Ge, T0 depends on the doping level and constant α ~ 0.5 (A.L. Woodcraft et al., J. Low Temp. Phys. 134 (2004) 925)
Mathi et al. 10.1109/WOLTE.2014.6881014
ln R varies linearly with T--0.5
A. Garai et al. Journal of Low Temp. 10.1007/s10909-015-1379-6

## Slide 15
Test with blank sapphire with Sn
Heater
Sapphire
NTD Ge sensor

## Slide 16
A cryogenic front-end pre-amplifier for bolometer
signal integration due to large cable capacitance, is prone to EMI noise due to longer length cables
Si-FET at cryogenic temperature of ~120 K intermediate 1st stage amplifier : designed, fabricated, tested in a Ln2 cryostat
A. Reza, V. Vatsa et al., J. Low Temp. Phys., 199, 200–205 (2020)
Low temperature electronics R&D
Analytical model for electronic noise is being developed
Since electrical noise is the dominating reason limiting the resolution of bolometer.
Bolometer readout circuit & equivalent noise model
Ideally the performance of a bolometer detector is expected to be superior due to its good intrinsic resolution. However, electronic noise is the limiting factor.

## Slide 17: TiLES (Tifr Low background Experimental Setup)
Detector surrounded by OFHC Cu (5 cm), Pb (10 cm) (210Pb < 0.3 Bq/kg).
N2 purging system and active muon veto (plastic scintillators)
TiLES is used for material screening such as ETP Cu, INO site rock, CsI crystals for DINO, etc.
Sensitivity of the setup:
~1 mBq/g ( ~10 ppb)
Roman Pb
Cu
Plastic Scintillator

## Slide 18
DBD to excited state in 94Zr
The current best experimental limits are T1/2 > 1.3 x 1019 y (68% C.L.) (Norman et al., Phys. Lett. B 195, 126 (1987)).
540 g of natZr (99.5% purity) counted in the TiLES,
Gamma ray spectra of natZr in TiLES for t = 7d
Decay Scheme of 94Zr
Double beta decay of 94Zr to the 1st excited state in 94Mo
T1/2 > 2.0 x 1020 y 68% C.L, 6.12 x 1019 y at 90% C.L..
N. Dokania et al EPJ A 53 (2017) 74

## Slide 19
MINT: Muon Induced Neutron detector setup at Tifr
Harisree Krishnamoorthy, NUPHYS2018
Gamma spectrum gated by muons in TiLES
Pb
Pb
HDPE
Muon detectors (plastic Scintillators)
Neutron detectors (CLYC)
Energy(keV)
Counts/(0.7 keV))
PSD
E
(n,n’g)
provides crucial input for validation of GEANT4.10.05 simulation of both muon induced neutron production and neutron inelastic scattering.
HK et al, EPJA 55 (2019) 136

## Slide 20
124Sn (n, ) 125Sn
125Sn : β decay →125Sb,
Qβ = 2357 keV
T1/2 = 9.52m, 9.64 days
125Sb β-decay → 125Te
(T1/2 =2.75 y, Qβ=766 keV)
124Sn (n, ) 125Sn (n, ) 126Sn
126Sn β- decay →126Sb
(T1/2 = 2.3 X 105 years, Qβ = 378 keV)
126Sb β-decay → 126Te
(T1/2 =12.35 days, Qβ = 3673 keV)
n-induced background in 124Sn
Simulation studies to estimate neutron flux at INO site based on rock composition carried out.
N. Dokania et al., JINST, 10 (2015) T12005
n-induced reactions in Sn, Pb, Cu are being studied at PLF and Dhruva
G. Gupta et al. ARI 158 (2020), 108923
(Qββ of 124Sn = 2293 keV )

## Slide 21
Several nuclear models to calculate the NTME
  Shell-model and variants
  QRPA and extensions
  Alternative models
The NTME (M2ν) is sensitive to details of the nuclear structure
  Spectroscopic properties of the initial and final nucleus
  Pairing and Deformation
Nuclear Structure Aspect
Uncertainty in estimated neutrino mass upto a factor of 10 due to uncertainty in NTMEs.
Observed physical properties of nuclei:Test of nuclear models
Experiments to constrain NTME are essential
A. Shrivastava et al. Phys Rev C105, 014605 (2022)
Occupational Probabilities of valence orbitals relevant to NDBD of 124Sn
Measurement of transfer cross-sections (d,p) (p,d), (4He,3He), (3He,4He) in 124Sn & 124Te

## Slide 22
0.22 % Sn-Bi is suggested as a good candidate for the fabrication of Sn-Bi bolometers.
Baking the TIN.TIN detector for a few minutes at 323 K would reduce the risk of tin pest.
Mazumdar, et al. Scripta Materialia 199 (2021), 113858
& Materials Research Express 6 (2019) 076521 ,
Studies on β <- -> α transition in Sn and Sn-rich alloys for a cryogenic tin bolometer (Tin pest problem)

## Slide 23
Radiation background studies relevant to rare decays
Measurements of muon induced neutron background and neutron capture gamma background carried out.
Aut rock studies (radiopurity and neutron activation) are carried out
low backgruond counting setup used for qualifying/screening materials :CsI crystals grown at BARC for DINO, Vizag, jadguguda, Jhakri, Atal , Zojila rock samples
D2O radiopurity measurements for DLS
Radionuclide | AUTB | BWH
232Th | 12±1 ppb | 338±14 ppb
238U | 60±2 ppb | 9±1 ppb
40K | <2 ppb | 2179±139 ppb
S. Thakur et al. , Nucl. Inst. Meth. A 1038 (2022) 166892
Notes: The neutron background is quite difficult to suppress

## Slide 24: Rock sample studies
Rock sample | Concentration(ppb) |  | 
 | 232Th | 238U | 40K
AUT | 12 | 60 | <2
Atal | 580 | 115 | 1304
Jhakri | 1924 | 1597 | 1334
Zojila | 1106 | 140 | 491
BWH | 338 | 9 | 2179
Sample Name | Mass (g) | Density (g/cc) | Counting time (d)
AUT | 27.50 | 2.93 | 23.4
Jhakri | 10.77 | 2.12 | 8.6
Atal | 6.89 | 2.96 | 28.9
Zojila | 130.02 | 2.75 | 19.77
Preliminary results

## Slide 25
After prototype demonstration
Build a large scale detector (~ 1 ton)
( 3phases: 100 Kg, 500 Kg, 1000 Kg)
Fn =G0n |M0n|2 = 8.569 x 10-13 yr-1 (PHFB)
= 1.382 x 10-13 yr-1 (SM)
With 90 % enrichment, background ~ 0.01 counts/ keV.kg.yr
mn~100 meV in 1 yr (SM) , mn~50 meV in 1 yr (PHFB)
…Future Goal..
Measurements with natSn bolometer using Am-Pu source
Rare decay studies using low BKG setup (DBD to excited state in 94Zr).
NTD Ge Sensor development (contd..)
2nbb measurements in 124Sn
…Next Step..

## Slide 26
24m x15 m x 3.5 m high
Space requirement and a possible layout
10m x10 m x 10 m high
Control + DAQ room
Low background counting lab 8m x6.5 m x 3.5 m high
Future expansion scope?

## Slide 27
http://www.tifr.res.in/~tin.tin/
Tin.Tin Collaboration
TIFR, Mumbai
Vivek Singh, Neha Dokania, S. Mathimalar,
A. Garai , Harisree krishnamoorthy,
Aparajita Mazumdar, Ghnashyam Gupta, Ashif Reza
Vishal Vatsa, Nishant Jangid
M.S. Pose, Mallikarjun
V. Nanal, V.M. Datar*,
S. Ramakrishnan*, R. Palit, S. Wategaonkar*
BARC, Mumbai
A. Shrivastava, K.C. Jagadeesan, S.V. Thakare,
Kamalesh Dasgupta, S.G. Nakhate, Soumen Bhattacharyya
IIT Ropar P.K. Raina, Pushpendra P Singh,
R.G. Pillay*, Swati Thakur
Univ. of Lucknow P.K. Rath
PRL V.K.B. Kota VECC Parnika Das

## Slide 28
http://www.tifr.res.in/~tin.tin/
Acknowledgement
Tin.Tin Collaboration
INO collaboration
Pelletron Linac Facility
& colleagues from TIFR-BARC

## Slide 29
Backup slides

## Slide 30
liquid 4He ~ 4.2 K, 3He ~ 3.2 K
Pumping on liq. 4He ~1.2 K, 3He ~ 0.3 K
Cooling through the continuous cycle of a 3He / 4He mixture for lower temperatures
How do we get mK temperature?
3He-4He Dilution Refrigerator
Fraction of 3He
Phase diagram for a mixture of 3He / 4He
When a mixture of the two isotopes of helium is cooled below a critical temperature, it separates into two phases.
The lighter "concentrated phase" is rich in 3He and the heavier "dilute phase" is rich in 4He. Since the enthalpies of the 3He in the two phases are different, it is possible to obtain cooling by "evaporating" the 3He from the concentrated phase into the dilute phase.
This process continues to work even at the lowest temperatures because the equilibrium concentration of 3He in the dilute phase is still finite even as the temperature approaches absolute zero.
(originally proposed by H. London in 1951)

## Slide 31
Make a natural Sn bolometric detector ~ 0.51 Kg
Radiation background studies
Detector and background simulations
Thermalization issues
  between the electronic and phononic systems
  ballistic phonons, single crystal vs polycrystalline Sn
Allotropic transition in Sn : the sample disintegrates due to a sudden increase in the volume, affects the longevity, alloying with Bi for suppression of tin pest
Vibration effect
Sensor development
Reliable NTME calculations
Enrichment of 124Sn
Constraining NTME, GT measurement in NDBD nuclei
Challenges in the 124Sn NDBD experiment

## Slide 32
N2 flushing in the TiLES
Radon produced in the natural decay chains of U and Th get trapped in the volume of the detector.
Boil-off nitrogen from LN2 cylinder at a pressure of ~8 mbar flowed in the volume around the detector setup kept inside a sealed Perspex box.
Gamma ray spectra of room background in TiLES (t = 7d)
Decay scheme of 222Rn (in 238U)

## Slide 33
Best Limits so far…
GERDA : (90% C.L.), 0.2-0.4 eV
(PRL 111 (2013) 122503)
KamLANDZen : (90% C.L.), 0.061-0.165 eV
(PRL 117 (2016) 082503)
CUORE : (90% C.L.), 0.140-0.400 eV
(arxiv :1710.07988,2017)
Experiment | Isotopes | (years) | <mee> eV
NEMO-3 | 48Ca | >2 x 1022 | 
GERDA- I | 76Ge | >2.1 x 1025 | 0.25-0.62
NEMO-3 | 100Mo | >1.1 x 1024 | 0.34-0.87
CUOROCINO | 130Te | >2.8 x 1024 | 0.31-0.76
EXO-200 | 136Xe | >1.6 x 1025 | 0.14-0.38
KamLAND-Zen | 136Xe | >1.07 x 1026 | 0.061-0.165
Experiment | Isotopes |  | <mee> eV
NEMO-3 | 48Ca | >2 x 1022 | 
GERDA- I | 76Ge | >2.1 x 1025 | 0.25-0.62
NEMO-3 | 100Mo | >1.1 x 1024 | 0.34-0.87
CUOROCINO | 130Te | >2.8 x 1024 | 0.31-0.76
EXO-200 | 136Xe | >1.6 x 1025 | 0.14-0.38
KamLAND-Zen | 136Xe | >1.07 x 1026 | 0.061-0.165
Current Science 112, 1375 (2017)
Direct neutrino mass measurement – KATRIN (3H, Q~18 keV , sensitivity ~ 0.2 eV), HOLMES +ECHO (163Ho- EC, Q ~ 2.55 keV, sensitivity < 2 eV), MARE (187Re, Q ~2.49 keV , sensitivity <0.2 eV)

## Slide 34: Utilities
5T electrical Crane
Chilled water
AHU
UPS
place for keeping compressors, pumps
Some of the labs need class 1000/10000 clean room
Change room/buffer access for personnel/equipment entering the assembly/process room
Control room
Surface labs

## Slide 35: The CFDR-1200 diagnostics
MC Temperature sensor: Speer, CMN, FPD(0.015-3.3K)
Automatic temperature control
Temperature stability ~0.1%, accuracy ~ 1 mK
Optically isolated RS232 adapter for PT and pressure gauge communications