## Slide 1
Discussion meeting on underground facility in India
A proposal for an underground facility for nuclear astrophysics
Satyaranjan Santra
Nuclear Physics Division
Bhabha Atomic Research Centre, Mumbai
6th August, 2022

## Slide 2
Discussion meeting on underground facility in India
Outline of the presentation
6th August, 2022
  Underground facilities for nuclear astrophysics
  Reactions of interest
  Present status of a few
  Proposed accelerator
  Proposal for AJT & RMS
  Summary

## Slide 3: Underground accelerator facilities around the World
SURF:Sanford underground Research Facility, South Dakota
CASPAR:Compact Accelerator System for Performing Astrophysical Research
Laboratorio Subterráneo de Canfranc (LSC), Spain
Agua Negra Deep Experiment Site, Argentina & Chile
6 Major facilities:
5 of them are very recent (within last 5 years)

## Slide 4: Flux attenuation at different underground labs
Facility | Depth | Flux attenuation |  | 
 |  | Muon | Neutron | Gamma
LUNA, Italy | 1.4 km, 3.1 kmwe | 10-6 | 10-3 | 10-3
JUNA, China | 2.4 km, 6.72 kmwe | 10-8 | 10-5 | 10-5
CASPER, USA | 1.49 km, 4.3 kmwe | 10-6 | 10-3 | 10-3
Felsenkeller, Germany | 50 m, 140 mwe | 4x10-1 |  | 4x10-1
CANFRANC (Spain) | 0.85 km, 2.5 kmwe | 5x10-7 |  | 
ANDES (S America) | 1.75 km, 4.5 kmwe | 10-6 |  | 
CARNFRANC
(CASPAR)
(LUNA)
(JUNA)

## Slide 5: Reactions of interest - 1
SL no. | Reactions | Physics | Gammow peak (keV) | X-section (barn) | Labs interested | Existing error | Reference
1 | 14N(p,g)15O | CNO | 148 | 10-13 | LUNA, CASPER |  | 
2 | 12C+12,13C | C burning | 820 | 10-13 (2.4 MeV) | LUNA |  | 
3 | 13C(a,n)16O | Heavy Ion synthesis, AGB | 300 | 10-16 | LUNA, JUNA, CUNA, CASPER | 60% | Astrophys. J., 414 (1993) 735
4 | 22Ne(a,n)25Mg | Heavy Ion synthesis, AGB |  |  | LUNA, CUNA, CASPER |  | 
5 | 22Ne(p,g)23Na | Synthesis in AGB stars | 190 | 2.4x10-3 (290 keV) | LUNA | Up to 3 orders | 
Same reaction is addressed by multiple labs  to reduce uncertainties using different techniques

## Slide 6: Reactions of interest - 2
SL no. | Reactions | Physics | Gammow peak (keV) | X-section (barn) | Labs interested | Existing error | Reference
6 | 12C(a,g)16O | Massive star | 300 | 10-17 | LUNA, JUNA | 60% | NPA, 758 (2005) 363
7 | 18O(p,a)15N | CNO | 160 | 3x10-5 (240 keV) | LUNA |  | 
8 | 19F(p,a)16O | F abundance | 100 | 7x10-9 | JUNA | 80% | PLB, 748 (2015) 178
9 | 25Mg(p,γ)26Al | Galaxy 26Al | 58 (reso) | 2x10-13 | JUNA | 20% | PLB 707 (2012) 60
Gamow energies ~ a few keV to 100’s of keV
Cross sections ~ as low as 10-17 barn  not possible to measure over ground due cosmic background

## Slide 7: 12C(a,g)16O, holy grail in Nuclear Astrophysics
  Felsenkeller: Carbon beam on helium gas target, inverse kinematics (13C(a,n)16O x-section is 5 order more, tgt contamination is a problem)
  Highly sought-after reaction data related to carbon/oxygen ratio in the Universe.
  JUNA approach: high-intensity alpha beam on carbon target

## Slide 8: Gamow energies for 12C(a,g)16O reaction at diff. sites
  Nearly all models of different nucleosynthesis environments are affected by the production of carbon and oxygen
  Precise (within 10%) determination of the reaction rate of 12C(a,g)16O is a key ingredient
  Propose to use inverse kinematics i.e., Carbon beam on helium gas target and Recoil Mass Separator

## Slide 9: 13C(a,n): S-process for Heavy Ion formation
Normalization of data under debate
Data unavailable in Gammow region
Beam from MV machine with inverse kinematics can be used covering a wide range of energies
RMS for background reduction

## Slide 10: 3He(a,g)7Be: PP chain & Li abundance
Affects i) hydrogen burning in Sun and production of ii) 7Li in Big bang nucleosynthesis and iii) 7Be and 8B solar neutrino fluxes.
Direct measurement data around Gamow peaks (25 and 250 keV) are sparse
Proposed underground accelerator facility can cover the entire energy (20-500 keV) of interest and RMS for background reduction

## Slide 11: 12C+12,13C fusion: 23Na/20Ne
Direct measurement data around Gamow peaks (<1 MeV) not available
12C(12C,pg)23Na and 12C(12C,ag)20Ne . Ratio of 23Na to 20Ne important
Proposed underground accelerator facilities can cover the entire energy of interest

## Slide 12: Required terminal voltage for proposed experiments
Maximum energy chosen to cover is 2 MeV, because
High energy data required for S-factor normalization
To avoid tail of resonances around 1 MeV for some reactions, normalization at higher energy required
Inverse kinematics and RMS to be used to reduce background

## Slide 13: Proposal for an underground accelerator facility
Phase I: 400 kV high current accelerator with an ECR source
Timeline = 2024-2034; Cost~140 Cr (excluding tunnel works)
  Space =50 m x 20 m Project duration=15 years Tentative cost=290 crore
Phase-II : 5 MV single ended ECR based Pelletron accelerator
Timeline=2034-2039, Cost~150 Cr)

## Slide 14: Implementation/Delivery
Year | Implementation/Delivery
Phase-I | 
1st – 3rd | Building of tunnels and caverns; design of laboratories, beam lines & experiments
4th to 7th | Procurement and commissioning of a 400 keV machine; setting up of experimental facilities including beam lines, detector array, target assembly and data acquisition system
7th – 10th | Phase-I activities including a few challenging experiments will be completed
Phase-II | 
11th – 15th | Procurement and commissioning of 5 MV machine; setting up of experimental facilities; Experiments using MV machine

## Slide 15: End of first presentation
Summary at the end of 2nd presentation

## Slide 16: AJT coupled to an RMS for deep underground measurements - J J Das
Nabajyoti Pandit
Dimpal Saikia

## Slide 17: CUPAC-NE Proposal for Underground facility
If the “accelerator system for nuclear astrophysics at INO site” is approved,
then
CUPAC-NE collaboration would like to participate in construction of some instrumentations of common interest:
  AJT ( Advanced Jet Target) Close loop supersonic Jet target
  An RMS of MD-ED-MD type (with rotation) with compact foot print
  Strictly monochromatic neutron source for investigation of s-process in AGB stars
  Explore extracting beam in space charge limited domain

## Slide 18: Advanced Jet Target system
Recirculation gas target >99% gases: 8 Roots blower, 10 1000l/s turbo pumps, compressors, filters and purifiers, exhaust system
Design of windowless gas target
Simplified scheme of the LUNA recirculation gas target
ORNL [Das2013]

## Slide 19: Recoil mass separator at Underground: first time
LUNA Data precision limited by backgrounds: natural, beam induced and target
RMS can provide a solution: NOT used underground so far
Inverse kinematicsinterchange target & projectile  improves accuracy: reduces systematic errors
CUPAC-NE-BARC Concepts: AJT+RMS
AJT: Reduce systematic errors (use 3He,3H gas target with recirculation target)
RMS: Eliminate beam and natural background and target impurity
Novel RMS design: very compact PIMS + HIRA ED1 slot+ RIB optics for IKR

## Slide 20: Recoil mass separator at Underground: first time
Novelty of the concept: MD-ED-MD similar to HIRA (ED-MD-ED)
Compact foot print, no quadrapoles, hardware corrections of aberrations
Spherical doubly focusing ESA (Electrostatic Analyzer) [Das 1997]
Anode slot like HIRA for High current operation [Sinha 1997]
Experience in ion optics: GIOS, GICOZY for inverse kinematic reactions IKR [Das 2005], SIMION 8.2
Propose: A Rotatable PIMS spectrometer: MD-ED-MD
Doubly focusing spherical ED, No quadrapoles
PIMS spectrometer

## Slide 21: HIRA spectrometer layout and optics
7Be
7Be ToF spectra
Momentum filter slits
RTS

## Slide 22: Investigation of s-process for neutron sources in AGB stars using monochromatic neutron source
Novelty of the concept:
Strictly monochromatic neutron beam, kinematic reconstruction
p(7Li,7Be)n at 14.5 MeV with 7Be kinematic coincidence
Normalization of neutron flux using counting of 7Be in PPAC
Neutrons produced in <1Sr forward solid angle due to IKR, so >90% contamination caused by backward scattered neutrons vastly eliminated.
Reconstruction of neutron energy from Be angle using kinematics
NOT done before

## Slide 23: Potential CUPAC-NE-BARC contribution : monochromatic neutron source
No neutrons
p(7Li,7Be)n at 14.5 MeV with 7Be in kinematic coincidence

## Slide 24: Potential CUPAC-NE contribution : Space charge limited beam extraction
Commercial accelerators don’t have space charge Compensation, current LIMIT <1 mA.
  Some hands on experience at Cotton
  Designed and implemented Space charge compensation at ISTF3, ORNL
Would like to explore ~5 mA
SIMION 8.0: Space charge can be estimated.
Gerald Alton suggested following:
Trap electrons by a negative electrode. High +ve charge of Beam attracts electrons and exits as space charge balanced beam

## Slide 25: Summary & conclusions
  A lot of opportunity exists to explore the reactions of interest to nuclear astrophysics, specially relevant to He and C, due to unavailability of data around the Gamow region and large uncertainties in experimental data
  To keep pace with the international community of nuclear astrophysics a deep (>1.5 km) underground accelerator facility is essential
  Proposed Accelerator facility, with 400 keV (phase-I) and 5 MV single ended (phase-II), will be able to cover the energy range of interest including inverse kinematics
  The above facility coupled with Recoil Mass Separator and windowless gas target will be a unique facility in the world
Thank you for your kind attention